PRODUCT SPECIFICATION – QuietZone Solserene Fabric Ceiling System

Section 09 80 00 Acoustical Treatment

Section 09 77 40 Noise Reduction Materials

Part 1 – GENERAL

  - Summary

Stretch-fabric system installed on retaining track system that provides drywall-like appearance with excellent sound absorptive qualities.  Can be used in any size room,  various ceiling styles and accommodates all lighting and HVAC systems.

  - Related Products

- Section 09 85 00 -QuietZone Acoustic Sealant

- Section 09 85 00 -QuietZone Acoustic Floor Mat

- Section 09 85 00 -QuietZone Acoustic Wall Framing

- Section 09 85 00 -QuietZone Acoustic Batt Insulation

- Section 09 54 00 –QuietZone Acoustyle Wood Ceiling System

  - Submittals

- Product Data:  Submit Owens Corning product literature, installation instructions and product samples for specified fabric ceiling.

  - Delivery, Storage and Handling

- Comply with manufacturer’s recommendations for handling, storage and protection during installation

- Must wear clean gloves when handling fabric.

Part 2 – PRODUCT

2.01 Manufacturer

A.  Owens Corning

One Owens Corning Parkway

Toledo, OH  43614

2.02 QuietZone Solserene Fabric Ceiling System

A.  Noise Reduction Coefficient (NRC)- .80, Type A mounting (ASTM C-423)

B.  Noise Reduction Coefficient (NRC)- 1.0, Type E-400 mounting (ASTM C-423)

C.  Class I rating according to ASTM-E84

D.  Light Reflectance- .75 to .80 for white fabric

Part 3 – EXECUTION

3.01 Inspection

A.  Examine the areas and conditions under which work of this section will be installed.  Verify that lighting and other penetration levels have been addressed.  Verify that project drawings comply with installation requirements.

B.  Provide written report listing conditions detrimental to the performance of work in this section.  Do not proceed with installation until unsatisfactory conditions have

been resolved.

3.02 Installation

A.  Comply with manufacturer’s instruction and recommendations for particular conditions of installation in each case.

B.  Mount fabric retaining tracks direct to drywall or to 1”x3” furring on joists.

C.  Set levels for penetrations.  May require extension boxes, alternate blocking or wood framing.

D.  Attach Acoustic core making joints as tight as possible.  Fill seams with acoustic caulk to prevent see-through.

E.  Fabric labeled for direction.  Carefully cut penetrations after fabric stretched into place.

3.04 Material Storage and Protection

A.   Protect ceiling system from damage.

B.   Store in a dry place, out of the elements.

END OF SECTION